## Slide 1
NETWORKING PROJECT · MULTIPATH TRANSPORT PROTOCOLS
MPTCP vs MP-QUIC
A Comparative Study of Multipath Transport Protocols
Kaushal Rathi 24110290
Krina Paghadar 24110169
Pratik Kumar Dhakar 24110277
Swamini More 24110211

## Slide 2
01 · MOTIVATION & SCOPE
Problem Statement & Objectives
WHY MULTIPATH?
Reliability — tolerate a path failure without dropping the connection
Throughput — combine bandwidth across simultaneously active paths
Real-world driver — mobile devices with Wi-Fi + cellular, dual-uplink servers, datacenter multi-homing
PROJECT OBJECTIVES
Compare MPTCP and MP-QUIC for video streaming, file transfer, and VoIP
Measure throughput, latency (RTT / jitter), and connection stability under controlled conditions
Analyze how each protocol handles packet loss and congestion
Recommend a protocol/scheduler by application need — not a single universal winner
SCOPE OF THIS PROJECT
MPTCP was fully implemented and measured across four controlled experiments (symmetric paths, asymmetric paths, packet loss, and mid-transfer path failure). MP-QUIC experiments were designed with an identical, mirrored topology for direct comparability — execution and measurement were still in progress within the project's two-week window (see Challenges Faced, slide 5). Where MP-QUIC results are not yet our own, comparisons draw on published literature, clearly marked as such.
MPTCP vs MP-QUIC
1

## Slide 3
02 · DESIGN
Architecture & Mechanism
MPTCP — KERNEL-LEVEL
MP_CAPABLE handshake negotiates multipath support (HMAC-SHA256 proof)
MP_JOIN adds a subflow: token + nonce + HMAC prove it belongs to the connection
Path manager opens subflows; kernel scheduler assigns packets by per-path RTT / cwnd
Design goal: “must resemble TCP on the wire” for middlebox compatibility
MP-QUIC — LIBRARY-LEVEL
Each path validated independently via PATH_CHALLENGE / PATH_RESPONSE
Per-path RTT + cwnd drive a MinRTT-style scheduler — no cross-path coupled window
Runs over UDP; multipath logic lives in the library (e.g. TQUIC), not the OS kernel
Failure detection is probe-driven, not TCP's RTO-based subflow timeout
TESTBED — MIRRORED FOR BOTH PROTOCOLS
Client
Server
Path 1 — 50 Mbps / 10 ms
Path 2 — varied per experiment (5-50 Mbps, 10-80 ms, 0-3% loss, or failed)
Tooling: Mininet + NetEm (topology & impairment) · iproute2 (MPTCP subflow / path control) · iperf3 (throughput) · Wireshark (packet capture)
MPTCP vs MP-QUIC
2

## Slide 4
03 · IMPLEMENTATION & RESULTS
Extension, Issues & Evaluation
MPTCP — MEASURED (4 EXPERIMENTS)
Exp | Scenario | Throughput (S/R, Mbps) | Path Split | Result
E1 | Symmetric (50/10 both paths) | 95.4 / 93.6 | 50% / 50% | As expected
E2 | Asymmetric (50/10 vs 5/80) | 52.5 / 51.2 | 91% / 9% | As expected
E3 | + 3% loss on Path 2 | 42.2 / 41.6 | 98% / 2% | As expected
E4 | Path 2 fails mid-transfer | 79.9 / 78.5 | survives, ~1-3s recovery | As expected
AGGREGATE THROUGHPUT BY EXPERIMENT
Chart: 
| E1 | E2 | E3 | E4
Sender Throughput (Mbps) | 95.4 | 52.5 | 42.2 | 79.9
MP-QUIC — EXPERIMENTAL DESIGN (MIRRORED, IN PROGRESS)
Same topology & parameters mirrored 1:1 onto MP-QUIC (E1-E4, plus an optional scheduler-comparison run E5)
Mechanistic prediction: a MinRTT-style scheduler has no cross-path fairness coupling, so the Path-1/Path-2 skew is expected to be sharper than MPTCP's in asymmetric runs (E2, E3)
Failure recovery (E4) is expected to take slightly longer than MPTCP's measured ~1-3s, since PATH_CHALLENGE / PATH_RESPONSE validation adds a round trip before failover is confirmed
Status: designed and ready to run; execution/measurement in progress at time of submission — see Challenges Faced
MPTCP vs MP-QUIC
3

## Slide 5
04 · QUALITY ATTRIBUTES
Non-Functional Testing Parameters
Parameter | MPTCP | MP-QUIC | Basis
Performance (throughput / RTT / jitter) | Near-linear aggregation on symmetric paths; skews toward the better path when asymmetric | Similar aggregation expected; sharper skew predicted (no coupled window) | Measured / Predicted
Reliability (path-failure tolerance) | Survives path loss; RTO-based detection, ~1-3s recovery (measured) | Survives path loss; probe-based (PATH_CHALLENGE) detection, expected slightly slower | Measured / Literature
Scalability (adding more paths) | Per-subflow kernel state; path manager overhead grows with subflow count | Paths are library-level over UDP; generally cheaper to add than kernel subflows | Literature
Fairness (vs. single-path TCP) | Coupled congestion control (LIA / OLIA / BALIA) protects shared-bottleneck fairness | No IETF-standardized coupling yet; fairness behavior is library-specific | Literature
Compatibility (middlebox traversal) | TCP-options-based; fragile where middleboxes strip unknown options | UDP-based; generally more middlebox-friendly, though some networks throttle UDP | Literature
Across every dimension, the two protocols make different trade-offs — neither dominates the other outright.
MPTCP vs MP-QUIC
4

## Slide 6
05 · LESSONS FROM THE FIELD
Challenges Faced
Kernel-level MPTCP configuration
Path-manager modes, per-subflow limits, and sysctls needed careful tuning — very different from configuring a userspace library.
Building a directly comparable topology
Mirroring identical Mininet/NetEm parameters (bandwidth, delay, loss) across a kernel stack (MPTCP) and a userspace library (MP-QUIC) so results stay comparable.
Two-week timeline
MPTCP experiments (E1-E4) were completed and validated. MP-QUIC experiments were fully designed and mirrored, but execution/measurement was still in progress at submission.
Scheduler heterogeneity
MPTCP's kernel scheduler and MP-QUIC library schedulers (e.g., TQUIC's MinRTT / Redundant) are not standardized the same way, complicating a strict apples-to-apples comparison.
MPTCP vs MP-QUIC
5

## Slide 7
06 · PUTTING IT TOGETHER
Comparative Summary & Recommendations
 | TCP | MPTCP | QUIC | MP-QUIC
Throughput | Single path only | Aggregates paths (measured) | Single path only | Aggregates paths (literature)
Failure tolerance | None — connection drops | Survives, RTO-based (~1-3s, measured) | Fast reconnect only | Survives, probe-based (literature)
Middlebox compatibility | High (ubiquitous) | Fragile — TCP-options can be stripped | Generally good (UDP-based) | Generally good, but UDP can be throttled
RECOMMENDATION BY APPLICATION — NO SINGLE PROTOCOL WINS OUTRIGHT
Video Streaming
Favor low-latency, redundancy-aware scheduling to protect QoE against jitter and path-loss spikes.
File Transfer
Favor coupled throughput aggregation (MPTCP-style) to maximize bulk-transfer bandwidth.
VoIP
Favor redundant multipath scheduling (either protocol) — trading bandwidth for resilience against loss/jitter.
MPTCP vs MP-QUIC
6